## Slide 1
PigmentCal-UQ
CAN YOU TRUST THIS NUMBER?
A reliability layer for pulse-oximeter readings
GREEN
AMBER
RED
ABSTAIN
Independent project · Pragatheesvar · Not a diagnostic device. Not clinically validated.
Notes: (30 s) A pulse oximeter shows one number and never tells you when that number should not be trusted. My project adds that missing warning. Transition: Why does the number sometimes deserve doubt?

## Slide 2
Problem Statement
One number. No warning about its reliability.
Not a diagnostic device. Not clinically validated. · Data shown is synthetic / simulated.
A single SpO₂ number hides how reliable it is
Weak pulse, noise and movement reduce reliability
Reliability may differ across pigmentation groups
Goal: know when NOT to trust the number
finger → light → “98 %” ?
Notes: (50 s) The device shines light through the finger. If the pulse signal is weak or noisy, or the person moves, the reading is less reliable. Reports also suggest reliability can differ with skin pigmentation. The screen shows only one number, so the user cannot see this. I do not claim to fix the number. I measure how far it can be trusted. Do not quote figures or citations you have not checked. Transition: So what does the system do?

## Slide 3
Proposed Solution, Innovation and Research Gap
Not a diagnostic device. Not clinically validated. · Data shown is synthetic / simulated.
Measure
Signal quality (SQI)
Perfusion (PI)
Objective pigmentation (ITA)
Calibrate
Conformal interval (CQR)
per ITA × PI group (Mondrian)
Decide
GREEN / AMBER / RED
or ABSTAIN when evidence is thin
Research gap
Implemented and tested in software. Coverage on real participants with arterial reference values is NOT yet shown.
Notes: (60 s) The system looks at signal quality, perfusion and an objective colour angle called ITA. It builds an uncertainty interval calibrated separately for each group. If a group has too little calibration data it says I do not know instead of guessing. The method is implemented and tested. The gap is that it has not been validated on real participants with blood-gas reference values. ITA is a colour measurement, not race. Transition: Here is how it is built.

## Slide 4
System Architecture and Technology Stack
Not a diagnostic device. Not clinically validated. · Data shown is synthetic / simulated.
ESP32 + MAX30102
(or virtual simulation)
→
Browser
React + TypeScript
→
FastAPI
Python
Research gate
hash-bound provenance
LIVE MONITOR
SQI, PI, estimated SpO₂ → rule engine
→ GREEN / AMBER / RED / ABSTAIN
(no calibrated interval)
RELIABILITY CHECK
Ridge / LightGBM → CQR → Mondrian (ITA × PI)
→ prediction interval + state
(abstains if group data is insufficient)
Python · FastAPI · scikit-learn · LightGBM · React · TypeScript · Web Serial
Notes: (55 s) There are two separate layers. The Live Monitor uses a transparent rule engine. The Reliability Check uses the calibrated interval. A research gate stops synthetic or simulated data from ever being shown as research results. Transition: Let me show it.

## Slide 5
Prototype Demonstration
Not a diagnostic device. Not clinically validated. · Data shown is synthetic / simulated.
VIRTUAL HARDWARE SIMULATION — NOT REAL MEASUREMENTS
A Normal signal
GREEN
B Low perfusion
AMBER (screenshot)
C High motion / combined
ABSTAIN (screenshot)
D Low perfusion + intermediate noise
RED (may fluctuate)
E Dark × Normal PI, calibrated layer
ABSTAIN — insufficient calibration
Notes: (90 s) Keep the banner visible and say once: these are simulated readings and the SpO2 shown is an uncalibrated estimate. Live set: A normal -> GREEN; D low perfusion + intermediate noise -> RED may appear and can fluctuate; E Reliability Check with ITA -10 -> ABSTAIN (insufficient Dark x Normal PI calibration: 8 participants, 44 rows, needs 10 and 30). B (AMBER) and C (ABSTAIN) from backup screenshots. Do not demo the phone camera or Web Serial. Say the live rule engine and the calibrated layer are separate. RED does not show a real oximeter is inaccurate or unsafe. Transition: That was a simulation, so here is what is and is not validated.

## Slide 6
Results, Validation Status and Limitations
Honest status: implemented and tested in software; research validation pending
Not a diagnostic device. Not clinically validated. · Data shown is synthetic / simulated.
Software tests
520 backend + 108 frontend passed
Synthetic pipeline
tested (180 virtual participants, invented rule)
Virtual hardware
tested for software integration
CQR / Mondrian
implemented — real empirical validation pending
Real research data
0
Real research validation
NOT AVAILABLE
Physical hardware / Wokwi
NOT TESTED / NOT EXECUTED
Clinical validation
NOT AVAILABLE
Notes: (65 s) The software works end to end. The models were trained on a synthetic dataset with a rule I invented, so its numbers prove the pipeline runs, not that it works on people. I have no real participant data yet and I have not tested the physical sensor. CQR and Mondrian are implemented; real empirical validation is pending. GREEN means only that no configured reliability flags were raised. Transition: So the path forward is clear.

## Slide 7
Conclusion and Future Scope
Not a diagnostic device. Not clinically validated. · Data shown is synthetic / simulated.
Built
Tested reliability framework
Signal quality + perfusion + ITA
Calibrated intervals per group
Abstains instead of guessing
Research gate for provenance
Next
Ethics approval and permissions
Paired reference SaO₂ + colour data
Participant-level validation
Subgroup coverage and width
Physical hardware test
Can you trust this number? Now the system can tell you when you should not.
Notes: (40 s) The contribution is a framework that tells you when not to trust a reading, built and tested end to end. Real validation is the next phase. Closing line: Can you trust this number? Now the system can tell you when you should not.